## Slide 1: PyBullet Tutorial
강영민
동명대학교

## Slide 2: PyBullet Quickstart Guide
https://docs.google.com/document/d/10sXEhzFRSnvFcl3XxNGhnD4N2SedqwdAvK3dsihxVUA/edit#
Easy to use Python model for physics simulation
  For robotics, games, visual effects and machine learning
  With a focus on sim-to-real transfer
File formats
  Urdf, sdf, mjcf…
Provides
  Forward dynamics
  Inverse dynamics
  Forward and inverse kinematics
  Collision detection
  Ray intersection queries
Bullet physics SDK
  Pybullet robotics
    Simulated minitaur quadruped, humanoids running using Tensorflow inference and KUKA arms grasping objects

## Slide 3: Other Features
Rendering
  CPU renderer
    TinyRenderer
  OpenGL Visualization
  Support for VR headsets
    HTC Vive, Oculus Rift
Built-in client-server support

## Slide 4: Hello PyBullet World
Pybullet 사용예

## Slide 5: Connect, disconnect
First thing to do
  Connecting to the physics simulation
PyBullet
  Client-server driven API
    Client sending commands and a physics server returns the status
Built-in Physics servers
  DIRECT
  GUI
DIRECT
  You cannot access the openGL and VR hardware features
  Allows rendering of images using the built-in software renderer through the getCameraImage API
    Useful for running simulations in the cloud on servers without GPU
getConnectionInfo
  Given a physicsClientId will return the list [isConnected, connectionMethod]

## Slide 6: Physics client (blue) and physics server (green) options

## Slide 7: Connect using DIRECT, GUI
DIRECT
  Sends the commands directly to the physics engine
    No transport layer and no graphics visualization window
    Directly returns the status after executing the command
GUI
  Creates a new graphics user interface with 3D OpenGL rendering
  GUI runs in a separate thread (Windows, Linux) – (OSX: GUI runs in the same thread)
    Commands and status messages are sent between PyBullet client and the GUI physics server using an ordinary memory buffer
  Another possibility
    Connect to a physics server in a different process on the same machine or on a remote machine using SHARED_MEMORY, UDP, or TCP networking.

## Slide 8: loadURDF, loadSDF, loadMJCF
loadURDF
  Sends a command to the server to load a physics model from a universal robot description file
    Used by Robot Operating System
    Created by WillowGarage and the Open source robotics foundation (OSRF)
  Most joints have motors enabled by default preventing free motion
arguments
+ optional arguments: flag, globalScaling, physicsclientId

## Slide 9: Save and restore / Collision shapes
Save and restore
  saveWorld
    Create an approximate snapshot of the current world as a pybullet python file
      Stored on the server
  saveState
  saveBullet
  restoreBullet
Collision shapes
  Easiest way to create stuffs
    Loading functions (urdf, sdf, mjcf, bullet)
  createCollisionshape
    Creates shapes for collision handling
  createVisualShape

## Slide 10: stepSimulation
Performs all the actiosn in a single forward dynamics simulation step
  Collision detection
  Constraint solving and integration
Default time step
  1/240 sec
  Can be changed using the setTimeStep or setPhysicsEngineParameterAPI
setRealTimeSimulation
  Run the simulation in real-time by letting the physics server automatically step the simulation according to its real-time clock (RTC)
  If you enable this, you needn’t call ‘stepSimulation’

## Slide 11: Transforms
Position
  Expressed in Cartesian world space coord
Orientations
  Quaternions
  Euler angles
  3x3 matrices
Functions
  getQuaternionFromEuler
  getEulerFromQuaternion
  getMatrixFromQuaternion
  multiplyTransforms, invertTransform
    Coordinate transformation

## Slide 12: Controlling a robot
Base, joints, links
  Urdf has a base
  Links are optional
    Connected by joints
getNumJoints
getJointInfo